## Slide 1
Hardware Security – Challenges and Directions
Selected Areas in Cryptography (SAC 2023)
Prof. Dr.-Ing. Tim Güneysu

## Slide 2: Digital Evolution and Security
>1950
>2020
Granularity
Implementation
Hardware
>1985
Hardware
Software
Hardware
Software
Security Demand
Networking & Connectivity
Physical Exposure
Privacy Requirements
How to partition security into hardware & software?
How much security can we achieve in hardware?

## Slide 3: Why a Root of Trust in Hardware is Essential
Hardware implementations are more efficient
    Boosts computationally exensive cryptography
    Less energy/area costs for constrained applicaitons
Protections in hardware are more powerful
    Opening up a hardware chip is assumed with higher cost compared to a disassembling a binary
    Some advanced countermeasures are only for hardware
Security-relevant components are hardware-only
    True Random Number Generators
0110001010001

## Slide 4: General Comparison: Software vs. Hardware (FPGA + ASIC)
Power/Energy consumption
Maintainability/ Flexibility
Performance
Development costs
Better
ASIC
FPGA
Notes: FPGA: best Trade-off (mittig und die schwächeren Vergleichszeichen sind immer zum besten hin)
Aber wie ist nun eine FPGA aufgebaut? Was macht ihn so atraktiv?

## Slide 5: Hardware Root of Trust – Directions and Challenges
Challenges
#1 Knowing the Adversary
#2 Preserving your Secrets
#3 Models and Limitations in Implementation Security
Directions
#1 Moving Target Defense in Hardware
#2 New Hardware Constraints for Cryptography
#3 Trusted and Security-oriented Hardware Design

## Slide 6: CHALLENGES
Knowing the Adversary

## Slide 7: CHALLENGE #1: Knowing the Adversary – Models and Boxes
Black-Box Attacker
Gray-Box Attacker
White-Box Attacker
x
y
k
k
Faulting security operations
Observing side-channel information
Analyzing gate-level components for vulnerabilities
Probing & modifying circuitry
COMPLEXITY
k
Observing & changing I/O data
Observing traffic patterns
Observing timing behavior

## Slide 8: CHALLENGE #1: Knowing the Adversary – Attacks in SW and HW
Logical Run-Time Attacks
    Boot attacks
    Software/Memory flaws
    Crypto primitive/protocol
  Physical Attacks
    Side-Channel analysis
    Fault-Injection Attacks
    Probing/Test port access
  IP Attacks
    Reverse engineering
    Cloning & modifications
    Trojans (HW & SW)
    Supply chain
How much protection does hardware offer?
Software
Hardware
Security Measures

## Slide 9: CHALLENGE #1: Knowing the Adversary – Model Mismatches
Even more prominent examples:
Megamos
Real attackers do no care about adversary models or laws
(Neither the public when your system is published to be broken)
The selection of choosing a minimal but holistic set of countermeasures is an underresearched topic

## Slide 10: CHALLENGES
Preserve Your Secrets

## Slide 11: CHALLENGE #2: Preserving your Secrets
SAC_CA_2023
SAC_CA_2023
Untrusted
Channel
ÜOc#2qß$Kqj
ÜOc#2qß$Kqj
e
k
e-1
k
Alice
Bob
ÜOc#2qß$Kqj
Oscar
Well-known Kerckhoff‘s Principle: only key k must be kept secret
 Cryptographer: „Hmm, that’s basically not my problem!“
 This needs to be solved by the implementation…

## Slide 12: CHALLENGE #2: Preserving your Secrets – SW vs. HW
Options in Software
    Where to put it? In the binary?
    Who then protects the binary? Using obfuscation?
    White-Box Cryptography (Fully broken, cf. DES, AES, DCA)
  Options in Hardware
    Secure distributed memories (ROM, Fuse, EEPROM, Flash, battery-backed BRAM)
    Physically Unclonable Functions (PUF)
Common Approach: Put some trusted components with key storage in hardware

## Slide 13: CHALLENGE #2: Preserving your Secrets – Hacking the Trusted HW
FLASH
RAM
EEPROM
Fuses
Analog
EEPROM security fuses as implemented inside a PIC16F886 microcontroller
EEPROM provides a security bit to enable readout protection of
Flash memory: 0 = none
1= protected

## Slide 14: CHALLENGE #2: Preserving your Secrets – Hacking the Trusted HW
Single EEPROM-cell covered with metal plate
UV-light Erasing Device

## Slide 15: CHALLENGE #2: Preserving your Secrets – Optical Side-Channels
Access to the surface of the chip from IC backside without creating contacts with internal wires
Optical interactions with transistors using Failure Analysis (FA) tools
Optical Techniques:
  Photon Emission
  Laser Stimulation
  Optical Probing
Boit, et al. "From IC Debug to Hardware Security Risk: The power of backside access and optical interaction," IPFA 2016.
Slide courtesy of Shahin Tajik, WPI

## Slide 16: CHALLENGE #2: Preserving your Secrets – Photon Emission Example
Assume an -bit counter in HW: clocked registers + some combinatorial logic
  The emission rate is proportional to the switching frequency
  Counter’s LSB is brighter than the MSB
  Clock buffers have the highest switching frequency >> The brightest spots are clock buffers
The emission of a counting counter on Intel/Altera MAX V (180 nm)
Tajik, et al. ”Emission Analysis of Hardware Implementations," DSD 2014.
Slide courtesy of Shahin Tajik, WPI

## Slide 17: Laser Logic State Imaging (LLSI)
Routing-based Trojan on Xilinx Kintex-7 (28 nm)
Intel/Altera Cyclone IV Register (60 nm)
Slide courtesy of Shahin Tajik, WPI
Without any countermeasures, secrets can be extracted just as a matter of time and cost from all conventional CMOS chips.
Combinations of protections (e.g., obfuscation, PUFs,…) can help to increase the complexity beyond practicability.

## Slide 18: CHALLENGES
Models and Limitations in Implementation Security

## Slide 19: Levels of Design Abstraction – Functional Perspective
Abstraction
System
Algorithm
Register Transfer
Gate
Circuit
Material
CPU
ROM
I/O
RAM
Low-Level Detail
How can we this combine with our security requirements, e.g., for SCA?
Notes: Information from: Introduction to Logic Circuits & Logic Design wiht Verilog (page 158)

## Slide 20: Side-Channel Attacks in Practice
Cryptographic Operation
Measure power consumption on execution
(Statistical) analysis to recover processed secret
Common Empirical Methods:
Simple Power Analysis (SPA)
Differential Power Analysis (DPA)
Correlation Power Analysis (CPA)
Test Vector Leakage Assessment (TVLA)

## Slide 21: Modeling Side-Channel Attacks
-probing model [ISW03]
An adversary is given the exact values of up to wires of a circuit .
Glitch-extended -probing model [FGP+18]
An adversary is given the exact values of all synchronization points influencing up to wires of a circuit .

## Slide 22: Advanced Models – Protection by Secure Gadgets
Insecure Circuit
Protected Circuit
Replace insecure gates by secure gadgets
Share inputs and outputs
Maintain timing (pipelining)

## Slide 23: Modeling Side-Channel Attacks – Composability
PNI [BBD+15]
Probe Non-Interference
PSNI [BBD+16]
Probe Strong Non-Interference
PINI [CS20]
Probe-Isolating Non-Interference
Similiar notions for fault injection attacks and the combined setting: FINI, CINI [FRSG22]

## Slide 24: Levels of Design Abstraction and SCA – The Security Gap
Abstraction
System
Algorithm
Register Transfer
Gate
Circuit
Material
CPU
ROM
I/O
RAM
Low-Level Detail
SPA DPA
CPA
TVLA
Constant
Time
ISW, PNI, PSNI, PINI
FINI, CINI
Formal
Verification
Testing and Practical Validation
THE GAP
Suitable complexity-aware sub-gate-level modelling is required for holistic verificaiton of implementation security
With a holistic view, root-cause analysis becomes feasible
???
???
Notes: Information from: Introduction to Logic Circuits & Logic Design wiht Verilog (page 158)

## Slide 25: DIRECTIONS
Moving Target Defense in Hardware

## Slide 26: DIRECTION: Moving Target Defense in Hardware
Many attack vectors exploit the static nature of hardware
Idea: Runtime reconfiguration of HW security components
Advantages:
Profiled and location-based attacks could be eliminated, e.g. SCA
Hardware could be upgraded on-the-fly in case of security failures
Runtime support for complex crypto portfolios (cf. NIST PQC standards)
Proof-of-Concept: Runtime-Dynamic AES Implementation on Hardware (FPGA)
Software
Secure
Hardware

## Slide 27: Proof-of-Concept Architecture – Runtime Reconfiguration of AES
FPGAs can be reconfigured in parts
Partial reconfiguration requires prebuilt subconfigurations (e.g. AES rounds)
All configuration data is stored on external flash and loaded by the PRC
Xilinx ZYNQ UltraScale+ SOC
PRC + ICAP
200 MHz
Partial Reconfiguration
AES Variations

## Slide 28: Proof-of-Concept Architecture – Design Concept – Top View
XCKU040-2FFVA1156E
Protected
AES
Encryption
Key Scheduler
UART/PCIe
Host
Key
Plaintext
Ciphertext
FSM
PRNG
ICAPe3
Partial Bitstreams
530 000 Logic Cells • 21.1 Mb BRAM

## Slide 29: Proof-of-Concept Architecture – Protected AES Encryption
40 differently implemented AES rounds • Arranged in a grid • Each column represents one AES round

## Slide 30: Proof-of-Concept Architecture – Protected AES Encryption

## Slide 31: Proof-of-Concept Architecture – Protected AES Encryption

## Slide 32: Proof-of-Concept Architecture – Protected AES Encryption

## Slide 33: Proof-of-Concept Architecture – Protected AES Encryption

## Slide 34: DIRECTION: Moving Target Defense in Hardware
Many attack vectors exploit the static nature of hardware
Idea: Runtime reconfiguration of HW security components
Disadvantages :
Limited countermeasure (x16) with high overhead in time and space
Runtime reconfiguration on FPGA is currently too slow (>10ms per run)
Formal security specification, verification and certification with dynamic hardware behavior even more complex
Future Directions:
Novel highly-reconfigurable FPGAs (as announced by Tabula but never released)
Neuromorphic computing to the rescue?
Software
Secure
Hardware

## Slide 35: DIRECTIONS
New Hardware Constraints for Cryptography

## Slide 36: New Hardware Constraints for Cryptography – Cache Design
Tag
Data
Caches are set-associative structures for improving memory access times
  Caches are table structure with ways and sets
  Set is determined by part of the address
  Way is determined by the replacement policy
0
1
2
1021
1022
1023
Index
Way 0
Way 1
Way 2
Way 3
…
…
…
…
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Index
Memory Address
Notes: Animationen

## Slide 37: New Hardware Constraints for Cryptography – Cache Design
Prime + Probe Attack
An attacker can observe cache accesses
  Fill a cache set
  Trigger victim access
  Re-Access eviction set
   Cache miss = access
There are even more sophisticated attacks
    Flush & Reload Prime Prune & Probe
0
1
2
1021
1022
1023
Index
Way 0
Way 1
Way 2
Way 3
…
…
…
…
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Index
Memory Address
Notes: Merge with previous slide

## Slide 38: New Hardware Constraints for Cryptography – Cache Design
Tag
Data
Cache randomization
  Prevents efficiently Prime + Probe attacks
  Index is pseudorandomly generated from the address
  Data is placed in one of the candidate entries
  Latest architectural proposal: ClepsydraCache [TNF+23]
What do we use as ?
0
1
2
1021
1022
1023
Index
Way 0
Way 1
Way 2
Way 3
…
…
…
…
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Memory Address
Tag
Index
[TNF+23] | Jan Philipp Thoma, Christian Niesler, Dominic A. Funke, Gregor Leander, Pierre Mayr, Nils Pohl, Lucas Davi, Tim Güneysu: ClepsydraCache - Preventing Cache Attacks with Time-Based Evictions. USENIX Security Symposium 2023
Notes: Animationen

## Slide 39: New Hardware Constraints for Cryptography – Cache Randomization
Functional Requirements
Low Latency Function will be part of cache design and must not decrease the access time
Key Dependency Secret and session-specific cache randomization
Invertibility (with a given tag) This is required to support write-back caches
Designed to match cache architectures (most recent caches have 1024 sets) Map 48-bit tag + 10-bit index to 10-bit randomized index Offset bits must be ignored
Memory Address
Tag
Index
48
10
10
Notes: Invertibility -> what does that mean? (figure)

## Slide 40: New Hardware Constraints for Cryptography – Attacker Modell
Attacker Model is different from what we usually assume in symmetric cryptography
  The attacker has never access to the output of
  The attacker can observe if two addresses collide
  The attacker aims to find colliding addresses

## Slide 41: New Hardware Constraints for Cryptography – Approaches
Approach 1: Use a low-latency block cipher (e.g. 64-bit PRINCE)
    Zero-pad 58-bit input and sample index-bits from ciphertext, use remainder as tag
    6 Bit storage overhead for the tag and comparison logic  expensive
Approach 2: Design a 58-bit block cipher
    Possible, but conventional design processes more (tag) data than required
    Ignores the weaker adversary model (no output available to attacker!)
Approach 3: Design a 10-bit cipher with reduced latency  SCARF [CGL+23]
[CGL+23] | Federico Canale, Tim Güneysu, Gregor Leander, Jan Philipp Thoma, Yosuke Todo, Rei Ueno: SCARF - A Low-Latency Block Cipher for Secure Cache-Randomization. USENIX Security Symposium 2023

## Slide 42: New Hardware Constraints for Cryptography – SCARF Cipher
SCARF is a 10-bit tweakable block cipher with 48-bit tweak and 240 Bit key
  Latency optimized combination of SPN and Feistel structure
Designed for 7 + 1 rounds
Further cryptanalysis welcome!
Notes: Hard part: Absorb the key in few rounds with low latency

## Slide 43: DIRECTIONS
Trusted and Security-oriented Hardware Design

## Slide 44: Trusted and Security-oriented Hardware Design
Abstraction
System
Algorithm
Register Transfer
Gate
Circuit
Material
CPU
ROM
I/O
RAM
Low-Level Detail
Hardware design EDA support optimization for performance, area and energy.
Support for security-oriented hardware design is required in EDA
Notes: Information from: Introduction to Logic Circuits & Logic Design wiht Verilog (page 158)

## Slide 45: Trusted and Security-oriented Hardware Design
Security-oriented design tool support is solely not sufficient
    Trust in development tools (external verification and validation required)
    Trust in manufacturing parties and supply chains
    Trust in delivery services
    Trust in key management and distribution services

## Slide 46: CONCLUSIONS

## Slide 47: Conclusions
Lessons Learned
Models of adversaries are fuzzy, better design for stronger ones
Secrets are hard to protect – hardware helps to make it harder
Models and abstractions are imperfect by nature, but often still too imperfect for implementation security
Moving target defense in hardware could disable profiling attacks
New hardware-oriented use-cases for cryptography emerge (such as fault-tolerant cryptography)
Trusted and secure design requires trusted and secure-oriented tools
47

## Slide 48
Thank you!
tim.gueneysu@rub.de

## Slide 49: References
[BBD+15] | Gilles Barthe, Sonia Belaïd, François Dupressoir, Pierre-Alain Fouque, Benjamin Grégoire, and Pierre-Yves Strub. Verified Proofs of Higher-Order Masking. In EUROCRYPT, pages 457–485, 2015.
[BBD+16] | Gilles Barthe, Sonia Belaïd, François Dupressoir, Pierre-Alain Fouque, Benjamin Grégoire, Pierre-Yves Strub, and Rébecca Zucchini. Strong Non-Interference and Type-Directed Higher-Order Masking. In SIGSAC, pages 116–129, 2016.
[CS20] | Gaetan Cassiers and Fran¸cois-Xavier Standaert. Trivially and Efficiently Composing Masked Gadgets With Probe Isolating Non-Interference. IEEE Trans. Inf. Forensics Secur., 15:2542–2555, 2020.
[DDE+20] | Joan Daemen, Christoph Dobraunig, Maria Eichlseder, Hannes Groß, Florian Mendel, and Robert Primas. Protecting against Statistical Ineffective Fault Attacks. IACR Trans. Cryptogr. Hardw. Embed. Syst., 2020(3):508–543, 2020.
[DN20] | Siemen Dhooghe and Svetla Nikova. My Gadget Just Cares for Me – How NINA Can Prove Security Against Combined Attacks. In CT-RSA, volume 12006 of Lecture Notes in Computer Science, pages 35–55. Springer, 2020.
[FGP+18] | Sebastian Faust, Vincent Grosso, Santos Merino Del Pozo, Clara Paglialonga, and Fran¸cois-Xavier Standaert. Composable Masking Schemes in the Presence of Physical Defaults & the Robust Probing Model. IACR Trans. Cryptogr. Hardw. Embed. Syst. , 2018(3):89–120, 2018.
[FRSG22] | Jakob Feldtkeller, Jan Richter-Brockmann, Pascal Sasdrich, and Tim Güneysu. CINI MINIS: Domain Isolation for Fault and Combined Security. CCS, 2022
[HPB21] | Vedad Hadzic, Robert Primas, and Roderick Bloem. Proving SIFA protection of masked redundant circuits. In Automated Technology for Verification and Analysis, volume 12971 of Lecture Notes in Computer Science, pages 249–265. Springer, 2021.
[ISW03] | Yuval Ishai, Amit Sahai, and David A. Wagner. Private Circuits: Securing Hardware against Probing Attacks. In Dan Boneh, editor, CRYPTO, volume 2729 of Lecture Notes in Computer Science, pages 463–481. Springer, 2003.
[TNF+23] | Jan Philipp Thoma, Christian Niesler, Dominic A. Funke, Gregor Leander, Pierre Mayr, Nils Pohl, Lucas Davi, Tim Güneysu: ClepsydraCache - Preventing Cache Attacks with Time-Based Evictions. USENIX Security Symposium 2023
[CGL+23] | Federico Canale, Tim Güneysu, Gregor Leander, Jan Philipp Thoma, Yosuke Todo, Rei Ueno: SCARF - A Low-Latency Block Cipher for Secure Cache-Randomization. USENIX Security Symposium 2023
[KSM20] | David Knichel, Pascal Sasdrich, and Amir Moradi. SILVER – Statistical Independence and Leakage Verification. In ASIACRYPT, volume 12491 of Lecture Notes in Computer Science, pages 787–816. Springer, 2020.
[RBRSS+21] | Jan Richter-Brockmann, Aein Rezaei Shahmirzadi, Pascal Sasdrich, Amir Moradi, and Tim Güneysu. FIVER – Robust Verification of Countermeasures against Fault Injections. IACR Trans. Cryptogr. Hardw. Embed. Syst., 2021(4):447–473, Aug. 2021.
[RBSG21] | Jan Richter-Brockmann, Pascal Sasdrich, and Tim Güneysu. Revisiting Fault Adversary Models - Hardware Faults in Theory and Practice. Trans. On Computers, 2022
[RFSG22] | Jan Richter-Brockmann, Jakob Feldtkeller, Pascal Sasdrich, and Tim Güneysu. VERICA - Verifi cation of Combined Attacks: Automated formal verification of security against simultaneous information leakage and tampering. IACR Trans. Cryptogr. Hardw. Embed. Syst. , 2022(4), 2022.
[SMG16] | Tobias Schneider, Amir Moradi, and Tim Güneysu. ParTI - Towards Combined Hardware Countermeasures Against Side-Channel and Fault-Injection Attacks. In CRYPTO 2016, volume 9815 of Lecture Notes in Computer Science, pages 302–332. Springer, 2016.

## Slide 50: Challenges
Challenges:
Static -> Dynamic HW
Embedding of Secrets (LVP, Obfuscation)
Models and Abstraction Levels (Fuzzy adversary model (faults))
Test & Validation
Cost of Countermeasures in Combined Settings
Trust in Components and Tools